## Slide 1: HDP October Status Update
Copper Balancing Part 2

## Slide 2: Total Copper Visualization
Pixel Size
  User defined
  Pixel count set small enough to capture traces and anti-pads
  Analysis time decreases as pixel count increases
Color Thresholds for Visualization
    Set “white” to a reference band
    (i.e. Design Average +/-10%)
    Red Hues above reference band
    Blue Hues below reference band

## Slide 3: Initial Board Design
Q3 == Q2 with smaller voids and added Cu under components
Q2 == Q1 with 20% thieving on 6 signal layers (4.6% added cu)
Q1
Q4
Q3
Q2

## Slide 4
Rolling average washes out high/low as expected
Captures general shape and symmetry patterns of large low copper areas - tracks with Phase 1 findings
Minimizes impact of small and large areas of stacked copper areas. The stand-off or glass stop conditions need to be captured.
0.5inch
1.25inch
2.5inch
Asymmetry of average thickness

## Slide 5: Color Thresholds
Changing color threshold mute or accnture patterns and gradient detail
White bands good for mapping areas to address with design
Full bands appear to have better visual correlation with Shado-Moire measurements
650um
0um

## Slide 6: Averaging vs Phase 1 Measurements
So far, the 1.5-2.5” radius averaging correlates well to many of the panels with high measured co-planarity
Next step is to look at refining algorithms to evaluate >2.5” averaging radius
Panel 2, Mtrl A
Panel 1, Mtrl B
650um
0um
Coplanarity of Q2 Shadow Moire
Total Cu map Q2 with rolling average of 2.5”

## Slide 7: Current Progress
Converted from VBA to Python to expand functionality
  3 separate algorithms for blending
    Gauss
    MetAve
    Step
Method to convert gerber to tiff to 2d array without MetAve or ‘Artwork’ software
Added preset color thresholds for analysis
Modified User Interface for more functionality

## Slide 8: MetAve Algorithm

## Slide 10: Future Work
Add thieving options